## Slide 1: Still Cracking: WPA2 Prevalence and Password Weakness in 2026
Dimitri Weaver
B-Sides
Buffalo
2026-06-06

## Slide 2: Agenda
01
02
03
04
05
06
Introductions & Disclaimer
Foundational Wi-Fi & Beacon Frames
WPA2 Authentication & 4-Way Handshake
What is PMKID & The 2018 Attack
Real-World Stats: WiGLE & Password Weakness
The Road Not Taken: Phase 2 & Mitigations
Confidential

## Slide 3: Meet the Speaker!
Dimitri Weaver
Not great at acronyms, spelling, or sitting still. Great at asking uncomfortable questions.
Dimitri Weaver
Former service member. Data analyst, helpdesk, sysadmin, & a supervisor. I break things in my free time.
Dimitri Weaver
I think like an attacker because I used to be one. Now I just do it with permission.
Dimitri Weaver
A kid at heart - curious about everything, sometimes things I probably shouldn't be.
Confidential

## Slide 4: WARNING! ALERT!
WARNING 2
DANGER!
DANGER!
WARNING 0
WARNING 1

## Slide 5: DISCLAIMER
NEVER, attempt capture or cracking of captured hashes of access points you do not have written consent to do so.
Unless, you like prison?
CFAA (18 U.S.C. § 1030) and state equivalents
Association with an AP without authorization is legally ambiguous and potentially prosecutable
CFAA (18 U.S.C. § 1030)
Accessing a computer without authorization is a federal crime. Association with an AP without consent is legally ambiguous and potentially prosecutable.
ECPA (18 U.S.C. § 2511)
Passive beacon receipt is protected under the public radio broadcast exception. Active PMKID capture occupies grayer legal territory.
State Law
NY Penal Law § 156 and equivalents in all 50 states add criminal exposure. Federal charges do not preempt state prosecution.
DOJ Good-Faith Research Policy (2022)
Good-faith security research should not be charged — but IRB approval, written authorization, and responsible disclosure are what establish good faith.
I am not a lawyer
I am not a lawyer
I am not a lawyer

## Slide 6
Password Assessment — Authorized Networks Only
Conducted entirely offline researcher-owned networks and consenting contacts with written authorization
Hashcat against captured hashes — RockYou
Credentials rotated by all participants post-study
Confidential
Research Methodology
Population Survey — Passive, Legal in All Jurisdictions
Kismet in monitor mode - beacon frames only, no association, no payload capture
Captured: SSID, BSSID, RSN IE security capabilities, signal strength
Target: ≥ 5,000 unique APs across a single US metro area
No greater risk to subjects than WiGLE.net or Google Street View Wi-Fi collection

## Slide 7: Foundational Wi-Fi
Confidential
10 times per second, every AP within range is announcing itself. No connection required.
SSID — the network name
BSSID — the AP's MAC address (first 3 bytes reveal the manufacturer)
RSN IE — security capabilities advertised by the AP: WPA/WPA2/WPA3, cipher suites
RSSI — signal strength, used as a proximity indicator
Channel — operating frequency band (2.4 GHz / 5 GHz)
Beacon frames are unencrypted and broadcast to all receivers by design - per IEEE 802.11.
No authentication or interaction with the network is required to receive them.

## Slide 8: Foundational Wi-Fi Continued
WPA2 4-Way Handshake
CLIENT (STA)
ACCESS POINT (AP)
MSG 1: ANonce (AP random nonce)
MSG 2: SNonce + MIC (proves PMK knowledge)
MSG 3: GTK + MIC (group key, encrypted)
MSG 4: ACK — session keys installed, encrypted traffic begins
ATTACKER NOTE: All 4 frames are observable in plaintext on the RF medium. PSK is never sent — but capturing MSG1+MSG2 gives everything needed to test password guesses offline. The crypto is not broken. The password is.
KEY DERIVATION
PSK (password) + SSID
↓ PBKDF2-SHA1 (4,096 iter)
PMK (256-bit)
↓ PRF-512 (PMK + nonces + MACs)
PTK (session key)
PTK = KEK + KCK + TK. Used for unicast encryption and MIC verification.
Confidential

## Slide 9: What is PMKID?
In 2018, Jens Steube - author of hashcat - discovered you can request the PMKID directly from the AP. No connected client. No deauth. One frame.
PMKID = HMAC-SHA1-128(PMK, "PMK Name" | MAC_AP | MAC_STA)
The PMK comes from your password. The MACs are public. The PMKID is in the air.
The PMKID - Pairwise Master Key Identifier - is a unique value the AP computes and includes in MSG 1 of the 4-Way Handshake. Originally designed to speed up roaming.
Confidential

## Slide 10: What is PMKID Continued
PMKID = HMAC-SHA1-128(PMK, "PMK Name" ‖ AA ‖ SPA)
AA - Authenticator Address. The AP's MAC address. Public. In every beacon frame.
SPA - Supplicant Address. The client's MAC address. Public. Visible to any observer.
PMK - Derived from your password. The only secret in the formula.
Confidential
Two of the three inputs are already public. The PMKID can be computed by anyone who knows the password — which means it can be tested against password guesses.

## Slide 11: PMKID Security Vulnerabilities
The Attack Chain
Step 1 : Run hcxdumptool targeting the AP. A single association request elicits EAPOL MSG 1 containing the PMKID. No connected client required. No deauth sent.
Step 2 : Convert the capture with hcxpcapngtool to .hc22000 format.
Step 3 : Run hashcat -m 22000 against a wordlist. Each guess = one PBKDF2-SHA1 computation. Weak password = game over. Fully offline. Zero detection.
Discovered in 2018 by Jens "Atom" Steube - the author of hashcat - while researching WPA3.
Confidential

## Slide 12: Real-World Stats: WiGLE & Password Weakness
74.76%
of observed networks run WPA2
3.22%
of observed networks run WPA3
1.73B
unique Wi-Fi networks in WiGLE database
Password Weakness: What the Research Says
Lim et al. (arXiv, Jan 2025) collected 3,352 WPA2 password hashes from live access points in Singapore.
Of those, 16% were recovered using dictionary and mask attacks in the study window. 8-digit numeric passphrases were broken in under 10 minutes. The study found widespread use of manufacturer default credentials and purely numeric passwords.
GPU crack times (DeepStrike, 2025): A 12-GPU RTX 5090 rig brute-forces an 8-character lowercase password in ~3 weeks.
With wordlists and rules, common passwords fall in minutes. A 12+ character random passphrase resists current cracking capabilities.
Confidential

## Slide 13: The Road Not Taken: Phase 2 & The Right Way To Do This
Phase 1 DONE: Passive Survey (US City)
Kismet in monitor mode, public streets only. Collected SSID, BSSID, RSN IE, signal strength. No payload capture. No association. No PMKID collection. Fully legal in all jurisdictions.
Results show WPA2 still dominant. Vendor OUI analysis reveals high-risk ISP-provisioned hardware. Full city-level data — location withheld per research protocol.
I stopped here. Phase 2 required authorization I did not have before this talk.
Phase 2: Active PMKID Collection
Requires: University IRB approval as institutional sponsor. Faculty PI of record. Full legal review of CFAA compliance under good-faith research doctrine (DOJ 2022 policy).
The talk you almost got: same data, with password crack rates, vendor OUI breakdown. That talk is coming.
Confidential

## Slide 14: What Actually Fixes This
01 Upgrade to WPA3
WPA3-Personal uses SAE (Simultaneous Authentication of Equals), eliminating offline dictionary attacks entirely. If your hardware supports it, enable it. Mandatory on all Wi-Fi CERTIFIED devices since July 2020.
02 Use a Strong Passphrase
On WPA2, password strength is the entire security model. 12+ random characters (letters, numbers, symbols) currently resists brute force. Never use phone numbers, dates, names, or ISP defaults.
03 Disable WPS
WPS PIN mode is trivially brute-forceable (8-digit PIN with checksum = ~11,000 guesses). Turn it off in your router admin panel.
04 Update Router Firmware
End-of-life routers receive no security patches. Hardware over 5 years old may lack WPA3 support entirely. Replace it.
05 Enterprise: Use 802.1X
WPA2-Enterprise with per-user certificates eliminates the shared PSK attack surface entirely. A cracked cert is useless without the private key.
Confidential

## Slide 15: Thank you!
Scan for Resources & References
anything@elrniracollage.lol
Confidential